## Slide 1: Benchmarking and HPL
CHPC SCC 2026 | LIVE PRESENTATION & DEMO

## Slide 2: What is “benchmarking”?
Measuring performance against a standard or competitor
Each team is a competitor
Each benchmark is unique and situational

## Slide 3: Benchmarking parameters
Kitchen |  | HPC
Waiting time (How long does the customer wait?) |  | FLOPS (Floating point operations per second)
Cost (How much does the food cost?) |  | Memory bandwidth (Memory data moved per second)
Daily production (How many can be prepared in a day?) |  | Storage read/write speed (How fast data moves to/from storage)
Taste (How good is the final meal?) |  | Accuracy (How precise the final calculation is)

## Slide 4: Floats, FLOPS and Matrices
Variable |  | Value
Temperature |  | 37.5°C
Velocity |  | 98.1 m/s
Pressure |  | 101.325 kPa
Pi |  | 3.14159
FLOPS (Floating Point Operations Per Second) 1 floating point operation:
A + B
2 floating point operations:
A * B + C
Computers use many floating point operations when solving matrix equations.

## Slide 5: The Synthetic Benchmark: HPL
Rank | System | Cores | Rmax (PFLOPS)
1 | LineShine (China) | 13,789,440 | 2,198.4
2 | El Capitan (US) | 11,340,000 | 1,809.0
3 | Frontier (US) | 9,066,176 | 1,353.0
4 | Aurora (US) | 9,264,128 | 1,012.0
5 | JUPITER Booster (Germany) | 4,801,344 | 1,000.0

## Slide 6: RPeak vs. RMax
RPeak is the theoretical maximum possible for the system.
RPeak = # of Nodes * # of Sockets per Node * # of Cores per Socket * CPU Frequency * Operations per cycle E.g. A compute node with 16 cores @ 4 MHz, using AVX512 Rpeak = (1) * (1) * (16) * (4 * 10^6) * (32)
= 1.229 GFLOPS
If the system has 4 identical compute nodes: 1.229 * 4 = 4.915 GFLOPS total
CPU Extension | Floating point operations per CPU cycle
SSE4.2 | 4
AVX | 8
AVX2 | 16
AVX512 | 32

## Slide 7: CPU core information
$ cat /proc/cpuinfo

## Slide 8: HPL configuration
N: total problem size
NB: block size
P * Q: total ranks
Threshold: residual comparison test value

## Slide 9: Problem size (N)
Run: echo | gcc -E -dM - | grep -E "SIZEOF_DOUBLE"
Set to a percentage so that memory usage doesn’t spill over into swap memory.
N should be a multiple of NB.

## Slide 10: Block size (NB)
Block size gets loaded into L2 cache
Use a multiple of the system’s cache line size
Recommended: 192 or 384 (Intel recommends 384 for Skylake architectures)
Important: Best to test empirically

## Slide 11: Total ranks (P * Q)
These need to match your MPI ranks
Keep P and Q as equal as possible. When not exact, use P<Q
Use Ranks = NUMA Nodes to limit need for communication
Note: Your virtual cluster only has 1 core per NUMA node

## Slide 12: NUMA
Non-Uniform Memory Access
Memory access is slower when remote

## Slide 13: Step-by-Step HPL Configuration
Choose block size (NB) – A multiple of cache line size; Fit to L2 cache size
Calculate problem size (N) – Keep some memory free for background tasks
Determine P * Q – Balance threads & ranks; Utilise NUMA
What about the rest of the options…?

## Slide 14: Other configurations
Threshold: value used for residual checks
BCASTs: how panel columns are sent to other processes
DEPTHs: how many panels to “look-ahead” while updating the current panel
SWAP: swapping algorithm used (binary exch. / spread-roll) – swapping threshold mixes the two if “mix” is used
RFACTs, PFACTs, NDIVs, and NBMINs control the HPL algorithm

## Slide 15: THANK YOU