## Slide 1
HPC Hardware
CHPC SCC 2026 | Selection Round
Building the machine you compete on
Live session + live node teardown demo

## Slide 2
What We're Covering Today
1
The Node
Anatomy of a compute server
2
The CPU
x86, ARM & what drives performance
3
RPeak
The one number that sets your ceiling
4
Memory
RAM channels & DIMM placement
5
Storage, Firmware & RAID
Disks, BIOS/CMOS, redundancy
6
Power + Live Demo
The budget, and meeting a real node

## Slide 3: Pop Kahoot Session
Join on kahoot.it!

## Slide 4
Why Hardware Matters in SCC
You are handed a fixed power budget and a fixed price list.
Every component you pick sets your theoretical ceiling before you run a single line of code.
Hardware
CPU - RAM - NIC
RPeak
Theoretical peak
HPL
Benchmark / Rmax
Score
Your ranking
SCC CONTEXT
You cannot out-optimise a bad hardware choice. Get the build right and the whole week - sysadmin, compilation, MPI, benchmarking - has a higher ceiling to chase. This feeds directly into the 'Putting Together a Cluster + Price List' session.

## Slide 5
From Data Centre to Chip
WHERE TODAY'S SESSION ZOOMS IN
Cluster Many nodes + a network fabric
Node One server: the box we open today
Socket / CPU One or more processors per node
Core Where the maths actually happens
Nodes are wired together with cables + a switch - that fabric is the HPC Networking session, next.

## Slide 6
Anatomy of a Compute Node
Server chassis (top view)
CPU + Heatsink
2x socket
RAM
DIMMs
Storage
SSD / NVMe
NIC
to network
PSU
AC -> DC power
Motherboard / PCIe
ties it together
RAM in channels ^
Six parts, one machine
CPU: does the maths
RAM: feeds the cores
Storage: holds OS + data
NIC: talks to other nodes
PSU: delivers clean power
Chassis: mounts + cools it all
We will open exactly this in the live demo.

## Slide 7
Power Supply (PSU)
WALL AC IN, CLEAN DC OUT
The PSU converts mains AC into the low-voltage DC rails the board needs (12V / 5V / 3.3V).
Rated in watts - it must cover every component at full load, with headroom.
Wall AC
230V
PSU
DC rails
12 / 5 / 3.3V
SCC CONTEXT
Power is a HARD ISC competition limit. Every watt burned in an inefficient PSU is a watt you cannot spend on compute under the cap. Higher efficiency = more useful cores for the same wall power. Redundant (1+1) PSUs exist for uptime - usually skipped in SCC.

## Slide 8
Server Chassis & Cooling
FORM FACTOR, DENSITY AND AIRFLOW
Measured in rack units (U) - 1U = 44.5 mm
1U
dense, hard to cool
2U
balanced - common
4U
roomy, big coolers
Airflow: cold front -> hot rear
Cold aisle in, hot aisle out - never recirculate.
SCC CONTEXT
Thermal throttling silently kills benchmark scores: a hot CPU drops its clock to survive, so RPeak you paid for never shows up. Cooling IS performance.

## Slide 9
Network Card (NIC)
THE NODE'S DOOR TO THE CLUSTER
Every node needs a way to talk to the others. The NIC is that door - on-board or a PCIe card.
MPI traffic between ranks rides this link, so its speed and latency matter for multi-node jobs.
1 GbE
basic / management
10 / 25 GbE
entry HPC
100 GbE
fast Ethernet / RoCE
InfiniBand
lowest latency, HPC standard
SCC CONTEXT
On multi-node runs the interconnect can become your bottleneck - my own HPL work showed network choices mattering hugely. Full detail in HPC Networking, next session.

## Slide 10
The CPU - Your Engine
SOCKETS, CORES, THREADS, CLOCK, CACHE
Socket
A physical CPU slot on the board. Nodes often have 1-2.
Core
An independent unit that executes instructions. More cores = more parallel work.
Thread (SMT)
Logical core sharing one physical core. Helps some workloads, not HPL.
Clock speed
Cycles per second (GHz). Each cycle a core can do several FLOPs.
Cache (L1/L2/L3)
Tiny, fast memory next to cores - keeps data close so cores don't stall.
One socket
16 cores
FLOPs = cores x clock x maths-per-cycle

## Slide 11
CPU Architectures: x86 vs ARM
TWO INSTRUCTION SETS, ONE TRADE-OFF
x86
Intel Xeon - AMD EPYC
+
Mature - runs everywhere
+
Highest per-core performance
+
Everything compiles, no surprises
-
More power per core
ARM
Grace - Ampere - Graviton
+
Best performance-per-watt
+
Very high core density
+
Huge memory bandwidth (Grace)
-
Some software still catching up
SCC CONTEXT
ARM is climbing the Top500 and Green500 fast. Under a power cap, performance-per-watt is what wins - but always check your competition apps actually compile on it first.

## Slide 12
RPeak - Your Theoretical Ceiling
RPeak is the absolute peak FLOP/s your hardware could ever hit. It is the number you are really buying when you choose CPUs.
RPeak =
nodes
x
sockets
x
cores
x
clock (GHz)
x
FLOPs/cycle
FLOPs/cycle depends on the vector unit: AVX2 = 16, AVX-512 = 32 (width x FMA x units).
SCC CONTEXT
More cores, higher clock, or wider vectors all raise RPeak - but so does power draw. The real game is maximising RPeak per watt and per rand. That is your build strategy.

## Slide 13
RPeak - A Worked Example
PLUG IN NUMBERS FOR A SMALL 4-NODE CLUSTER
Nodes
4
Sockets / node
2
Cores / socket
16
Clock
2.5 GHz
FLOPs / cycle
16 (AVX2)
4 x 2 x 16 = 128 cores
128 x 2.5 GHz x 16
= 5,120 GFLOP/s
= 5.12 TFLOP/s (RPeak)
RPeak
5.12 TF
theoretical
Rmax (~75%)
~3.8 TF
measured by HPL
SCC CONTEXT
Efficiency = Rmax / RPeak. HPL typically reaches 60-90%. RPeak sets the ceiling; the Benchmarking session measures how close you actually get.

## Slide 14
Your Turn - Calculate RPeak
A REAL TRI-NODE CLUSTER - THE SPEC SHEETS ARE ON THE INTERNET. PHONES OUT.
SWITCH
HEAD NODE (x1)
1 x Intel Xeon Silver 4310
login · scheduler · shared storage
COMPUTE NODE 1
2 x AMD EPYC 7313 (dual socket)
runs the HPL benchmark
COMPUTE NODE 2
2 x AMD EPYC 7313 (dual socket)
runs the HPL benchmark
YOUR TASK
1 Look up each CPU: cores + base clock + vector support
2 Work out FLOPs/cycle for each (previous slide)
3 Calculate RPeak of the two compute nodes
4 Bonus: whole-cluster RPeak - should the head node even count?
HINTS
Use the BASE clock, not boost. RPeak = nodes x sockets x cores x clock x FLOPs/cycle. Spec sheets: ark.intel.com / amd.com
~10 minutes. Work as a team - split the two CPUs between you.

## Slide 15
Your Turn - The Answer
WHAT THE SPEC SHEETS SHOULD HAVE TOLD YOU
Intel Xeon Silver 4310 (head node)
12 cores · 2.1 GHz base · AVX-512, 2 FMA units = 32 FLOPs/cycle
AMD EPYC 7313 (compute, 2 per node)
16 cores · 3.0 GHz base · AVX2 = 16 FLOPs/cycle
head : 1 x 12 x 2.1 x 32 = 806.4 GFLOP/s
compute : 2 x 16 x 3.0 x 16 = 1,536.0 GFLOP/s each
2 compute nodes = 3,072.0 GFLOP/s
+ head node = 3,878.4 GFLOP/s
COMPUTE RPeak = 3.07 TFLOP/s
the ceiling HPL will chase
CLUSTER TOTAL = 3.88 TFLOP/s
only if the head node joins the run
SCC CONTEXT
Most teams leave the head node OUT of the HPL run - it is busy with the scheduler, storage and monitoring. Quote 3.07 TF as your ceiling. Classic trap: the Xeon runs AVX-512, so it does 32 FLOPs/cycle, not 16 - the spec sheet is where marks are won.

## Slide 16
Memory (RAM) - Feeding the Cores
HPC IS OFTEN BANDWIDTH-BOUND, NOT JUST COMPUTE-BOUND
Two things matter:
Capacity - enough GB to hold the problem.
Bandwidth - how fast data reaches the cores.
DDR4 vs DDR5 - newer = more bandwidth.
ECC - server RAM that self-corrects bit errors.
CPU
cores
RAM
DIMMs
Wide, fast pipe = cores never wait
SCC CONTEXT
A cluster with fast cores but starved memory bandwidth runs far below RPeak. Balanced memory is one of the cheapest ways to protect your score.

## Slide 17
RAM Channels & DIMM Placement
THE CHEAPEST PERFORMANCE YOU CAN LOSE
A CPU reads memory over several channels in parallel. Populate one DIMM per channel to unlock full bandwidth.
GOOD: 4 sticks, all channels
CPU
ch A
ch B
ch C
ch D
Full 4-channel bandwidth
BAD: same 4 sticks, 2 channels
CPU
ch A
ch B
ch C
ch D
Up to HALF the bandwidth
Same RAM, same cost - placement alone decides. Always populate symmetrically and match speeds.

## Slide 18
Storage
ROLES MATTER MORE THAN RAW SIZE
OS disk
Boots the node, holds the system
Scratch
Fast local space for running jobs
Shared / NFS
Home dirs + data, seen by all nodes
Media: speed vs cost
HDD
cheap, big, slow
~0.2 GB/s
SATA SSD
fast, affordable
~0.5 GB/s
NVMe SSD
very fast, pricier
~3-7 GB/s
SCC CONTEXT
HPL barely touches storage - but real apps, datasets and checkpoints do. Don't overspend on storage you won't use under the power and budget cap.

## Slide 19
Firmware: BIOS / UEFI & CMOS
WHERE THE NODE'S LOWEST-LEVEL SETTINGS LIVE
UEFI/BIOS is firmware on a flash chip - the first code that runs at power-on.
CMOS holds your settings, kept alive by a small coin battery. Flat battery = settings reset.
Flash
CMOS
battery-backed
Performance toggles that matter
Disable deep C-states / power saving
Set 'performance' / 'max' power profile
SMT on or off (test per workload)
NUMA settings for memory locality
Set correct boot order
BIOS tuning is free performance.

## Slide 20
RAID - Software vs Hardware
COMBINE DISKS FOR SPEED OR SAFETY
RAID 0
stripe: speed, no safety
RAID 1
mirror: safety, half space
RAID 5/6
parity: balance
RAID 10
stripe + mirror
Hardware RAID
Dedicated card + battery-backed cache
Offloads parity from the CPU
Costs money, power & a failure point
Software RAID
mdadm / ZFS on the host CPU
Free, flexible, portable
Uses a little CPU + memory
SCC CONTEXT
For a benchmark cluster, RAID is usually unnecessary overhead - it spends power and money on resilience you don't need for a few HPL runs. Know it; rarely use it in SCC.

## Slide 21
Redundancy - and Why SCC Skips It
YOU'RE BUILDING A SPRINTER, NOT A 24/7 SERVER
Production data centre
Redundant (1+1) power supplies
RAID mirrors on every disk
Spare / failover nodes
Goal: 99.999% uptime
Your SCC cluster
One PSU per node is fine
No RAID on compute nodes
No idle spare nodes
Goal: peak for a few runs
SCC CONTEXT
Every watt and every rand spent on resilience is one NOT spent on FLOPs. The competition rewards peak performance over a handful of runs, not uptime - so skip redundancy and pour the budget into compute.

## Slide 22
Demo - Meet a Real Node
WE OPEN THE CHASSIS AND FIND EVERY PART WE JUST DISCUSSED
1
The chassis
airflow path, where parts mount
2
CPU & heatsink
lift the cooler, see the socket
3
RAM in channels
note which slots are filled
4
The NIC
the node's link to the cluster
5
Storage
the boot + scratch drive(s)
6
PSU
where wall power comes in
[ Live: physical node(s) on the table - swap in your own cluster photos on each card ]

## Slide 23
Demo - What the OS Sees
MAP EVERY PHYSICAL PART TO A COMMAND
$ lscpu
sockets, cores, threads, clock, arch (x86/ARM), cache
$ lscpu | grep Flags
vector units: avx2 / avx512 -> FLOPs/cycle
$ free -h / dmidecode -t memory
RAM size, speed and how channels are filled
$ lsblk
storage devices and partitions
$ lspci | grep -i net
the NIC on the PCIe bus
$ nproc / cat /proc/cpuinfo
quick core count + per-core detail
If the part is in the box, the OS can show it - this is how you verify a build.

## Slide 24
Common Mistakes & Misconceptions
!
More cores = always faster
Ignores memory bandwidth and the power cap.
!
Sloppy RAM placement
Wrong slots can halve your bandwidth, free of charge.
!
Forgetting the power cap
Biggest build doesn't win - best FLOPs/watt does.
!
Leaving BIOS on power-save
Cores quietly throttle; benchmarks tank.
!
Confusing RPeak with Rmax
Theoretical ceiling vs what HPL actually achieves.
!
Paying for redundancy
RAID/spare PSUs you'll never need in SCC.

## Slide 25
Key Takeaways
1
A node = CPU + RAM + storage + NIC + PSU in a chassis; nodes + network = a cluster.
2
RPeak = nodes x sockets x cores x clock x FLOPs/cycle - maximise it under the power cap.
3
x86 is safe and universal; ARM wins performance-per-watt - check your apps compile.
4
RAM bandwidth feeds the cores - populate every channel, symmetrically.
5
BIOS / firmware tuning is free performance - don't leave it on power-save.
6
For SCC, skip redundancy: optimise for peak, not uptime.

## Slide 26
What's Coming Next | Q&A
HPC Networking
The fabric that wires these nodes together - right after this.
System Administration
Configuring and provisioning the node you just met.
Cluster + Price List
Turn your RPeak maths into real purchasing decisions.
Benchmarking & HPL
Measure Rmax against the RPeak we just computed.
Questions?

## Slide 27
HPC Hardware - CHPC SCC 2026

## Slide 28
CPU Architecture: Von Neumann vs Harvard
ONE MEMORY, OR TWO?
Von Neumann
One shared memory for code + data
+
Simplest: one memory, one bus
+
Program is just data - easy to change
+
What general-purpose CPUs use
-
Shared bus = the von Neumann bottleneck
Harvard
Separate memory for code + data
+
Code + data fetched in parallel
+
No instruction/data bus contention
+
Common in microcontrollers + DSPs
-
Rigid; treating code as data is hard
SCC CONTEXT
Reality check: both x86_64 and ARM are von Neumann in main memory but modified Harvard at the L1 cache - split instruction + data caches give parallel fetch. x86 vs ARM is really CISC vs RISC, a different axis.

## Slide 29
How a Core Runs Code: The FDES Cycle
FOUR STEPS, REPEATED BILLIONS OF TIMES A SECOND
1 Fetch Control unit reads the next instruction; the program counter advances
2 Decode Work out what the instruction means and which unit + operands it needs
3 Execute The ALU, FPU or vector unit performs the actual operation
4 Store Write the result back to a register or memory - then loop to Fetch
Clock speed (slide 9) is how many of these cycles run per second - FLOPs/cycle is the maths the Execute step does each pass.